## Slide 1: Water Heights (altimetry): the satellites / sensors
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 2: Altimetry missions used in hydrology
1991
2032
Today
1991
1997
2003
2009
2015
2021
2027
3181 jours
7/17/1991 - 3/31/2000
ERS-1 (Esa)
4910 jours
8/10/1992 - 1/18/2006
Topex/Poseidon (Nasa/Cnes)
5921 jours
4/21/1995 - 7/6/2011
ERS-2 (Esa)
3692 jours
3/1/2002 - 4/8/2012
Envisat (Esa)
4130 jours
6/20/2008 - 10/10/2019
Jason-2 (Cnes/Eumetsat/Nasa/Noaa)
4286 jours
4/8/2010 - 12/31/2021
Cryosat-2 (Esa)
3232 jours
2/25/2013 - 12/31/2021
Saral (Cnes/Isro)
2559 jours
1/17/2016 - 1/18/2023
Jason-3 (Eumetsat/Noaa/Cnes/Nasa)
2558 jours
2/16/2016 - 2/16/2023
Sentinel-3A (EU)
2499 jours
3/31/2018 - 1/31/2025
Sentinel-3B (EU)
2557 jours
11/15/2020 - 11/15/2027
Jason-CS/Sentinel-6A (Esa/Eumetsat/Nasa)
1097 jours
2/15/2022 - 2/15/2025
Swot (Nasa/Cnes)
2558 jours
7/1/2023 - 7/1/2030
Sentinel-3C (EU)
2558 jours
7/1/2025 - 7/1/2032
Sentinel-3D (EU)
2558 jours
11/15/2025 - 11/15/2032
Jason-CS/Sentinel-6B (EU/Eumetsat/Nasa)
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 3: Altimetry satellites, from open ocean to rivers
A technique born to measure the ocean (first in 1969). First satellites (1970s) had a 1-m accuracy
1990s: ERS-1, Topex/Poseidon used over lakes, large rivers
Envisat & Saral, then Sentinel-3, Jason-2 & follow-on continues on these measurements
Saral: higher spatial resolution (smaller beam)
Cryosat-2, Sentinel-3A&B: use of synthetic aperture techniques (« division » of the beam in smaller units by processing the radar echo)
2022: Swot, an interferometric wide-swath imager
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 4: ERS-1 & 2
Esa
Launched: 17 July 1991 (ERS-1)
21 April 1995 (ERS-2)
End of mission: June 1996 (ERS-1)
June 2011 (end of global coverage in June 2003 for ERS-2)
Mission: To observe the Earth and its environment
Altitude: 782 to 785 km
Payload instruments:
  Single-frequency radar altimeter (RA)
  Dual-frequency radiometer (MWR)
  Laser for orbit determination
Orbit:
  Inclination: 98.52°
  Revisit frequency: 35 days 3 days (ERS-1 ice phase) 168 days (ERS-1 geodetic phase)
  Inter-track distance at the equator: 80 km (35-day cycle)
© ESA
© ESA
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 5: Topex/Poseidon
Nasa/Cnes
Launched: 10 August 1992
End of mission: 5 January 2006
Mission: To measure the height of the oceans
Altitude: 1,336 km
Payload instruments:
  Dual-frequency altimeter (Topex)
  Experimental single-frequency altimeter (Poseidon-1)
  3-frequency radiometer (TMR)
  Orbit determination: laser (LRA), Doris, GPS (GPSDR)
Orbit:
  Inclination: 66° (non sun-synchronous)
  Revisit frequency: 10 days
  Inter-track distance at the equator: 315 km
© Cnes/D. Ducros
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 6: Jason-1
Cnes/Nasa
Launched: 7 December 2001
End of mission: 1st July 2013
Mission: To measure the height of the oceans
Altitude: 1,336 km
Payload instruments:
  Dual-frequency altimeter (Poseidon-2)
  3-frequency radiometer (JMR)
  Orbit determination: Laser (LRA), GPS (TRSR), Doris
Orbit:
  Inclination: 66° (non sun-synchronous)
  Revisit frequency: 10 days
  Inter-track distance at the equator: 315 km
Satellite emission/reception scheme was not optimized for inland water, so few data available over lands
© Cnes/D. Ducros
© Cnes/D. Ducros
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 7: Envisat
Esa
Launched: 1 March 2002
End of mission: 9 May 2012
Mission: To observe the Earth and its environment
Altitude: 800 km
Payload instruments: 10 different instruments including:
  Radar altimeter (RA2)
  Radiometer (MWR)
  Orbit determination: laser (LRR), Doris
Orbit:
  Inclination: 98.5° (sun-synchronous)
  Revisit frequency: 35 days
  Inter-track distance at the equator: 80 km
© Esa
© Esa
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 8: Jason-2
Eumetsat/Noaa/Cnes/Nasa
Launched: 20 June 2008
End of mission: Oct. 2019
Mission: To measure the height of the oceans
Altitude: 1,336 km
Payload instruments:
  Dual-frequency altimeter (Poseidon-3)
  3-frequency radiometer (AMR)
  Orbit determination: laser (LRA), Doris, GPS (TRSR)
Orbit:
  Inclination: 66° (non sun-synchronous)
  Revisit frequency: 10 days
  Inter-track distance at the equator: 315 km
© Cnes/D. Ducros
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 9: Cryosat-2
Esa
Launched: 8 April 2010
Mission: To observe the polar regions
Altitude: 717 km
Payload instruments:
  Interferometric altimeter (Siral) (delay-Doppler instrument (SAR-mode))
  Orbit determination: Doris, laser (LRR)
Orbit:
  Inclination: 92° (non sun-synchronous)
  Revisit frequency: 369 days (although every point on the globe observed in 30 days)
© Esa
© Esa
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 10: Saral
Cnes/Isro
Launch: 25 February 2013
Mission: To observe the oceans
Altitude: 800 km
Payload instruments:
  Altimeter-radiometer AltiKa
  Orbit determination: laser (LRA), Doris (+ Argos3 instrument)
Orbit:
  Inclination : 98.5 ° (sun-synchronous)
  Revisit frequency: 35 days
  Inter-track distance at the equator: 80 km
© Cnes/Mira Production
© Cnes
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 11: Jason-3
© Cnes/D. Ducros
Eumetsat/Noaa/Cnes/Nasa
Launch: 17 January 2016
Mission: To measure the height of the oceans
Altitude: 1,336 km
Payload instruments:
  Dual-frequency altimeter (Poseidon-3B)
  3-frequency radiometer
  Orbit determination: laser , Doris, GPS
Orbit:
  Inclination: 66° (non sun-synchronous)
  Revisit frequency: 10 days
  Inter-track distance at the equator: 315 km
© Nasa/JPL
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 12: Sentinel-3
European Union
Launch: Sentinel-3A 18 February 2016;
Sentinel-3B 25 April 2018 (coming: C&D)
Mission: deliver routine operational services to policy-makers and marine and land service users
Altitude: 814.5 km
Payload instruments:
  Altimeter (Sral) C/Ku band follow-on Cryosat Siral (delay-Doppler instrument)
  Radiometer (dual-frequency)
  Orbit determination : laser (LRR) , Doris, GNSS
Orbit:
  Inclination: 98.65° (sun-synchronous)
  Revisit frequency: 27 days
© Esa
© Esa
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 13: Sentinel-6 (Jason-CS)
Esa/Eumetsat/EU/Noaa/Cnes/Nasa
Launch: Nov. 2020 (A / Michael Freilich) & 2025 (B)
Mission: To measure the height of the oceans, continuing the T/P-Jason series
Altitude: 1,336 km
Payload instruments:
  SRAL-based “Poseidon-4” altimeter (delay-Doppler instrument)
  radiometer
  Orbit determination: Doris, laser, GNSS
Orbit:
  Inclination: 66° (non sun-synchronous)
  Revisit frequency: 10 days
  Inter-track distance at the equator: 315 km
© Cnes/D. Ducros
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 14: Swot
Nasa/Cnes/CSA/UKSA
Launch: December 16, 2022
Mission: better understanding of the world's oceans
and its terrestrial surface waters.
Altitude: 890 km
Payload instruments:
  Interferometric altimeter (KaRIN)
  Nadir dual-frequency altimeter (Poseidon-3)
  3-frequency radiometer
  Orbit determination: Doris, laser, GPS
Orbit:
  Inclination: 77.6 °(non sun-synchronous)
  Revisit frequency: ~21 days (20.86455 days)
© Cnes/Mira Production
© TAS
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 15: Data access
Hydroweb http://hydroweb.theia-land.fr/?lang=en&
Copernicus Global Land https://land.copernicus.eu/global/products/wl
Database for Hydrological Time Series of Inland Waters (DAHITI) https://dahiti.dgfi.tum.de/en/
Global Reservoirs and Lakes Monitor (G-REALM) https://ipad.fas.usda.gov/cropexplorer/global_reservoir/
Rivers & Lakes (no longer updated) : http://altimetry.esa.int/riverlake/shared/main.html
FDR4Alt: new processing being fine-tuned https://www.fdr4alt.org/
Notes: Except otherwise noted, “Water heights (altimetry): the satellites / sensors” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0