## Slide 1: Swot in a nutshell
Notes: Except otherwise noted, “Swot in a nutshell” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 2: The Swot mission
Partnership between NASA, CNES, the Canadian Space Agency and the UK space agency,
A new concept, wide-swath interferometric altimetry (KaRIn)
  two 50-km swaths
  a bi-dimensional image
  All weather, night & day measurements
Data
  Direct measurements: water level, slope, width
  Indirect measurements: discharge, tidal velocities and amplitudes, wave heights, current velocities…
© Cnes/Mira Production
Notes: Except otherwise noted, “Swot in a nutshell” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 3: Swot for hydrology
Satellite measurements:
  Water height (in 2D),
  width,
  slope
Inferred data: discharge
Number of observations of France rivers and lakes during a 21-day cycle
Classical altimetry vs Swot around the Dead Sea (left, classical altimetry, measurements are only under the colored lines ; right, with Swot, measurements are all over the whitened areas)
© Cnes
Notes: Except otherwise noted, “Swot in a nutshell” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 4: The Swot mission
Rivers
Coastal area
Ocean
Lakes / reservoirs
Inferred measurements
  Height
  Water volume
  Height
  Surface slope
  Runoff
  Height
  Tidal velocities and amplitudes
  Current velocities2
  Wind speed3
  Wave amplitude
  Floating Objects
Current application examples
  Monitoring of water quantity variations in large lakes (a few hundred km2) ex: the drying of Aral Lake seen by Topex/Poseidon
  Currently no possibility
1. In bold: the quantities measurable directly by Swot. the others are obtained with models/interpolations completed possibly by other measurements
2. Deduce slope measurements from dynamic ocean topography and oceanographic modelling
3. Requiring a scatterometer
Swot's contribution
  Coverage of small lakes and reservoirs from 250 m x 250 m
  Coverage of all rivers wider than 100 m (50 m target)
  Application to submesoscale (< 300 km)
  Better accuracy and mitigation of perturbations
  Best resolution (to be confirmed)
  Possibility to visualize the coasts for the first time thanks to a better resolution
  Monitoring of water level and variations in large rivers ex: Amazon floods seen by Topex/Poseidon
  Measurement of Gulf Stream velocity fields by Envisat
  Hurricane Isabel Tracking by Jason-1 and Envisat
  Southern swell measurements (~ten meters) by Jason
  Search and rescue tracking of boats by SAR (resolution according to speed / surface state)
Notes: Except otherwise noted, “Swot in a nutshell” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0

## Slide 5: The Swot mission
oceanography
Collected data
Possible applications
hydrology
Quantity of water stored in lakes, rivers, reservoirs and other wetlands
Change in stored water quantities
Estimation of the discharge of large rivers
Water sharing management (international & interregional)
Better modelling of floods
Freshwater management for urban, industrial and agricultural consumption
Management of hydroelectric production
Preventing the spread of epidemics,
Estuary management
Help to inland navigation
enable …
Coastal currents
Representation of marine eddies at mesoscale scale
High resolution global ocean altimetry
Ocean Bathymetry
More accurate weather and climate forecasts
Help to navigation and rescue operations at sea
Assistance to fishermen
Assistance to oil platforms
enable…
Overview of Swot potential application fields
Notes: 5
Except otherwise noted, “Swot in a nutshell” presentation by Cnes/Aviso is licensed under CC BY-SA 4.0. To view a copy of this license, visit https://creativecommons.org/licenses/by-sa/4.0